## Slide 1: ARDUINO
BY: Excess Nepal

## Slide 2: What is Arduino??

## Slide 3
  Arduino is an open-source
  Flexible electronics prototyping platform
  easy-to-use hardware and software.
  Intended for artists, designers, hobbyists, and anyone interested in creating interactive objects or environments.

## Slide 4: 2.0 HARWARE OVERVIEW

## Slide 5: DIGITAL PINS
Digital Pin (0-13)
State: HIGH or LOW i.e 1 or 0
Use as Digital Input and Output
pinMode (PIN,MODE)
PIN: 0-13
Mode : INPUT / OUTPUT

## Slide 6: DIGITAL PINS AS INPUT
Read the value from specified pin
Either HIGH or LOW
Pin can be specified as either a variable or constant(0-13)
digitalWrite(Pin,HIGH);

## Slide 7: DIGITAL PINS AS OUTPUT
Write the value to specified pin
Either HIGH or LOW
Pin can be specified as either a variable or constant(0-13)
digitalWrite (pin, HIGH);

## Slide 8: ANALOG PINS READ
Analog pin (0-5)
Read the analog value from specified pin
Resulting integer value 0 to 1023
Do not need to first declared as INPUT OR OUTPUT
analogRead(PIN);

## Slide 9: ANALOG PINS WRITE
analogWrite(PIN,VALUE)
using hardware enabled pulse width modulation(PWM)
This function works on the pin 3 , 5 , 6 , 9 and 11

## Slide 10: Download and installation Arduino IDE
Arduino IDE software download from the official site of Arduino
The site is arduino.cc

## Slide 11: Programming Syntax
// - Single line comment
/* */ - Multiline comment
{ } – used to define a block of code that starts and ends.
; - used to define the end of a line of code.

## Slide 12: PROGRAMMING - VARIABLES
= (assignment) For example, x = 10*2, thus x = 20.
% (modulo) – this gives the remainder when one number is divided by another. For example 12 % 10 gives 2.
+ (addition)
- (subtraction)
* (multiplication)
/ (division)

## Slide 13: COMPARISON OPERATORS
== (equal to) - For example 12==10 is FALSE and 12 ==12 is TRUE.
!= (not equal to) - For example 12!=10 is TRUE and 12!=12 is FALSE.
< (less than)
> (greater than)

## Slide 14: PROGRAMMING - CONTROL STRUCTURE
if(condition) { }
else if (condition) { }
else(condition) { }
This will execute the code between the curly braces if the condition is true, and if not test the condition of the “else if”. If that is false , the “else” code will execute.
for (int i =0; i < #repeats; i ++) { }
Used when you would like to repeat a line of code a specific # of times. Often called a FOR LOOP.

## Slide 15: SUMMARY TO ARDUINO UNO
      Microcontrollers AT mega 328
      Operating Voltage 5V
      Digital I/O Pins 14 (of which 6 provide PWM output)
      Analog Input Pins 6
      DC Current per I/O Pin 40 mA
      Flash Memory 32 KB (of which 0.5 KB used by bootloader)
      SRAM 2 KB (ATmega328)
      Clock Speed 16 MHz

## Slide 16: LED BLINKING
Component required:
Arduino UNO R3
LED
Jumper wires
Breadboard
330 ohm resistor

## Slide 17: breadboard
A breadboard is a construction base for prototyping of electronics
A test platform for developing electronic devices.

## Slide 18: Breadboard contd….
A-B-C-D same terminal
4 pair of horizontal power supply terminals

## Slide 19: LED
Emits light when a small current passes through it
Schematic Symbol
It only works in ONE
direction. So make sure you
attach it correctly. Also it
often needs a resistor to
limit the current going to it.
Longer Led is Positive

## Slide 20: Appropriate resister
Restrict / limit the amount of electrical current
Protect LED from burn
Schematic Symbol

## Slide 21: Selection of Resistor

## Slide 22: Connection Diagram

## Slide 23
Its coding time……

## Slide 24: Program explanation
void setup ( ) { } - All of the code within the curly braces will be run ONCE when the program first runs.
void loop ( ) { } - This function is run AFTER setup has finished. All of the code within the curly braces will be run again, and again, until the power is removed.

## Slide 25
        Thank you